## Slide 1
Time for a new SIG
Special Interest Group for Time & Frequency Networks
Guy Roberts
Senior Network Architect
SIG-NGN, Bergen
9/9/2024

## Slide 2: SIG-TFN
In February at a meeting of NRENs and metrologists it was agreed to create a new SIG
This will be a new community which brings together NRENs and metrology
There is already strong interest: sig-tfn@lists.geant.org has 100 subscribers

## Slide 3: SIG-TFN
GÉANT is the coordinator of SIG-TFN
Web page: https://community.geant.org/sig-tfn/
There are two working groups within the SIG-TFN:
  T/F Sustainability (led by Richard Lui)
  C-TFN technical specification (Led by Guy Roberts)
We will have the first in-person SIG-TFN meeting in Amsterdam on the 16/17th Oct 2024. https://wiki.geant.org/display/SIG/1st+SIG-TFN+meeting+-+Amsterdam%2C+Netherlands

## Slide 4: C-TFN sustainability working group
Team
  Richard Lui
  Raphaël Marion
  Christian Chardonnet
  Wojbor Bogacki
  Christian Lisdat
  Davide Calonico
Objectives
Investigate a path to sustainability of the CLONETS-DS C-TFN, both for GÉANT and for participating NRENs and NMIs.
Carry out cost modelling to identify the extent of the future funding needs for fibre and flywheels
Engage EURAMET, NRENs, GÉANT and the European Commission to find solutions to long-term funding.

## Slide 5: C-TFN technical specification working group
Team
  Guy Roberts
  Jochen Kronjaeger
  Raphaël Marion
  Krzysztof Turza
  Jacques-Olivier Gaudron
Objectives
Expand on the CLONETS-DS architecture and integrate lessons learnt from PTB-PSNC pathfinder.
Investigate if tiers of flywheel performance are needed e.g NMI flywheel, NREN flywheel, etc.
Prepare a technical specification for the C-TFN flywheels.
Prepare a technical specification for the GÉANT should build their cross-border fibre links.

## Slide 6: Summary of use cases
Supplement GNSS with a fibre network to increase reliability of time distribution
Support the redefinition of the SI second being carried out between now and 2030 by NPL, PTB, Syrte and INRIM.
Perform fundamental physics research e.g. gravity wave experiments.
Support European-wide commercial services such as very accurate time stamps for banks to validate high-frequency trading.

## Slide 7: So what can GEANT/NRENs do?
National TF fibre networks are fragmented, without a coordinated plan to integrate them into a unified network (CLONETS-DS)
GÉANT and NRENs can build a unified network based on federating existing national time/frequency distribution infrastructures
Invest in coordination between NRENS and NMIs to build a sustainable community
Identify long-term funding beyond 2027

## Slide 8: How things stand today
NMI Frequency reference
Hut for housing RLS
Research institute
IRE
METAS
Bern
NPL
London
OP
Paris
OB
Brussels
PTB
Braunschweig
CERN Geneva
Strasbourg
Prague
ISI
Brno
GUM
Warsaw
PSNC
Poznan
Munich MPI
UMK
Torun
Cieszyn
Slubice
Lille
INRIM
Turin
Grenoble
Modane
Ostrava
Karlsruhe
Milan
ILNAS
Luxembourg
Basel
BEV
Vienna
Trieste
Ljubljana
Zagreb
CESNET
VSL
Delft
UvA
Innsbruck
Lithuania
Frequency network:
Green links built by NRENs in collaboration with national NMIs
Blue links built by local NMIs/researchers
NMIs:
Four big NMIs are involved in redefining the SI second highlighted in red
Wroclav
Hradec
Kralove

## Slide 9: What is missing?
NMI Frequency reference
Hut for housing RLS
Research institute
IRE
METAS
Bern
NPL
London
OP
Paris
OB
Brussels
PTB
Braunschweig
CERN Geneva
Strasbourg
Prague
ISI
Brno
GUM
Warsaw
PSNC
Poznan
Munich MPI
UMK
Torun
Cieszyn
Slubice
Lille
INRIM
Turin
Grenoble
Modane
Ostrava
Karlsruhe
Milan
ILNAS
Luxembourg
Basel
BEV
Vienna
Trieste
Ljubljana
Zagreb
CESNET
UvA
Innsbruck
Lithuania
Missing:
National based networks need to be interconnected
Eastern and Western islands of frequency services are not linked
A full ring/mesh of the big four NMIs will enable them to complete definition of the SI second
Link will also be needed to Nordics, SE and SW Europe as they develop Optical clocks
Wroclav
Hradec
Kralove
VSL
Delft

## Slide 10: Proposed solution
IRE
METAS
Bern
NPL
London
OP
Paris
OB
Brussels
PTB
Braunschweig
CERN Geneva
Strasbourg
Prague
ISI
Brno
GUM
Warsaw
PSNC
Poznan
Munich MPI
UMK
Torun
Cieszyn
Slubice
Lille
INRIM
Turin
Grenoble
Modane
Ostrava
Karlsruhe
Milan
ILNAS
Luxembourg
Basel
BEV
Vienna
Trieste
Ljubljana
Zagreb
CESNET
UvA
Innsbruck
Lithuania
Solution:
Red lines are proposed for GN5-2
These will interconnect national ‘islands’ of frequency networks
Support redefinition of the SI second
Primary users are national frequency reference providers
Secondary users are research institutes that connect via their national frequency provider
Wroclav
Hradec
Kralove
NMI Frequency reference
Hut for housing RLS
Research institute
VSL
Delft

## Slide 11: Proposed solution
IRE
METAS
Bern
NPL
London
OP
Paris
OB
Brussels
PTB
Braunschweig
CERN Geneva
Strasbourg
Prague
ISI
Brno
GUM
Warsaw
PSNC
Poznan
Munich MPI
UMK
Torun
Cieszyn
Slubice
Lille
INRIM
Turin
Grenoble
Modane
Ostrava
Karlsruhe
Milan
ILNAS
Luxembourg
Basel
BEV
Vienna
Trieste
Ljubljana
Zagreb
CESNET
UvA
Innsbruck
Lithuania
Solution:
Ring supports the four big NMIs that are part of the campaign for redefinition of the SI second
Wroclav
Hradec
Kralove
NMI Frequency reference
Hut for housing RLS
Research institute
VSL
Delft

## Slide 12: Architecture: services overlay fibre links
GEANT C-TFN
NREN C-TFN
flywheel / frequency comb
NMI
NMIs
Build, own and operate the T/F equipment:
  Flywheels, counters, frequency combs
Retain ownership of time/frequency
Generate and measure time/frequency
Terminate T/F services
Transport of T/F services
Time/freq. service overlay
RLS
NMI access point
GEANT, NRENs
build, own and operate transport links:
  fibre, amplifiers, access points, intermediate RLS
Provide a service to NMIs to carry T/F services
RLS
Ch. 45
NMI access point
WR
ELSTAB
Ch. 46
Ch. 44
flywheel / frequency comb
NMI
RLS
Ch. 45
WR
ELSTAB
Ch. 46
Ch. 44
Frequency service instance
White Rabbit service instance
ELSTAB service instance

## Slide 13: Frequency or White Rabbit on GEANT internet fibre?
After detailed investigation we decided it was not feasible to mix frequency with data on existing GÉANT fibre due to limitations of our DWDM equipment.
For this reason, dedicated fibre is recommended for frequency distribution.
NRENs such as SURF and CESNET are deploying White Rabbit on their dark fibre networks.
Could GÉANT put WR on our network?
  possibly, pending further tests
  either in the L-band links
  or overhead channels
L-band routes in the GEANT network
Because of frequency distribution requirements, the C-TFN will need dedicated time/frequency distribution fibre

## Slide 14: Benefits to NRENs of the C-TFN
Enhanced Knowledge Exchange and development expertise By sharing knowledge and best practices with NRENs, this initiative fosters the development of specialized expertise in time and frequency network deployment and management.
Strengthened Collaboration between NMIs and NRENs The initiative acts as a bridge, enhancing the flow of information and support between National Metrology Institutes (NMIs) and NRENs.
Direct Engagement with the Research Community: By working closely with researchers, GÉANT and NRENs can contribute significantly to the development of science data repositories and scientific workflows.
Opportunities for New Services and Applications: The expanded capabilities of the C-TFN will enable NRENs and GÉANT to explore and offer new non-data services, potentially opening new opportunities for collaboration in diverse scientific and commercial sectors.
Contribution to European Scientific Leadership: By fostering an integrated European T/F network, this initiative significantly contributes to Europe's standing as a global leader in high impact scientific research and technology.

## Slide 15: Pathfinder system
First proof-of-concept link for the CLONETS C-TFN, the purpose is to prove both frequency and time transfer
GÉANT fibre is now in place from PTB to the polish border and PSNC fibre to Poznan
Amplifier and RLS equipment installation is happening now
Bi-directional amp
Regenerator laser station
ELSTAB

## Slide 16: C-TFN Timeline
2024: build and Pathfinder link and prepare C-TFN
2025 - 2027: Build TFN Phase 1
After July 2027: TFN Phase 2 (funding not yet identified)
GN5-2 project preparation
2024 (GN5-1)
2025-27 (GN5-2)
C-TFN build, commissioning, operation
Pathfinder link Poznan-Braunschweig
April GN5-2T workplan agreed
Run procurement
Q4 2024
GEANT gate for procurement

## Slide 17: Conclusions
GÉANT is building two new fibre links:
  France-Belgium-Netherlands-Germany-Poland in 2025
  Italy-Austria-Germany-Czechia-Poland in 2026
GÉANT coordinates the requirements of both NMIs and NRENs in SIG-TFN along with its specialist sub-groups
Sustainability efforts will identify GÉANT, NREN and NMI funding for 2027 and beyond

## Slide 18
Thank You
Any questions?
www.geant.org