## Slide 1: Streaming Telemetry
Joao_Silva@ASR
‘
‘Not everything that can be counted counts and not everything that counts can be counted’
Albert Einstein

## Slide 2: HLD in 2019 for -> RCTS 2.0 building blocks
Transport Layer based on Segment Routing (ti-lfa) as Unified Forwarding Plane
Service Layer for Layer 2 (EVPN) and Layer 3 VPN services based on BGP as Unified Control Plan
SDN - Segment Routing Path Computation Element (SR-PCE) to provide simple and scalable inter-domain transport connectivity and Traffic Engineering and Path control
Visibility and Automation
  Streaming Telemetry to enhance visibility and monitoring
  NSO/Ansible for service provisioning with Netconf/YANG data models
We are Here!!!!

## Slide 3: Hidden Agenda
In this session we will:
-> Drive your motivation to kill SNMP!
Notes: Well, not literally, but yeah, to migrated when possible if the hardware supports streaming telemetry

## Slide 4: Motivation
If this is a picture of your NOC personnel…
You may have a Finger-Defined Network.
How do you monitor your Network?
Notes: This was a typical day, everything was fine on the network, but the equipments sometimes failed to respond to snmp messages

## Slide 5: Why change
For us, personally:
Switches logs full of messages: “%SNMP-3-RESPONSE_DELAYED: processing GetNext of entSensorType (150023 msecs)”, too many SNMP collectors
Routers: Change of default values in control-plane policies to accommodate the rate of snmp requests
Inability to fetch important data in equipment's, ie: evpn/perf-meas/bgp afi’s-safi’s
Short spaced glitches where very hard to see
Plan in motion to:
-> Improve visibility to help troubleshoot = faster problem resolution
Notes: Embarc+amos numa viagem no princpio deste ano sobre esta temática, para aprender e experimentar numa primeira fase e depois implementar

## Slide 6: “Pushing” More Data Really Does Work Better

## Slide 7: streaming telemetry stack

## Slide 8: First things, first: Telemetry stack
So, what is all this fuss about Streaming Telemetry…
Real-time data collection and transmission for monitoring.
Continuous and automated delivery of telemetry data.
Faster issue detection and response.
Enables historical data analysis.
Relies on efficient and reliable protocols.
Provides visibility into network and system operations.
Optimizes performance, enhances security, ensures reliability.
“Scream Stream If You Wanna Go Faster”
Notes: In a lab in cisco live2023 we realized the implementation was not so difficult. We are not going very deep, since this was taken from a hour long presentation on FCCN “TNC” from last year

## Slide 9: Data model layer
Raw data maped to a model
(YANG models: Native, OpenConfig, etc)

## Slide 10: Yang data models, this is where all begins
In the present day, a router has about 1300 Native models and 100 OpenConfig models
Native Models
OpenConfig Models
Aaaa, and IETF too….
Notes: Existem ainda modelo o ietf mas possuem ainda uma expressão muito pequena

## Slide 11: How to explore Yang data models
YangSuite
Notes: Cisco YANG Suite provides a set of tools and plugins to learn, test, and adopt YANG programmable interfaces such as NETCONF, RESTCONF, gNMI and more.
Its vendor agnostic and you can upload yang models directly from the router or switch, or from github.
Its downloadable in a container, easy to install go try it

## Slide 12: Configuration vs operational
Notes: Existem ainda modelo o ietf mas possuem ainda uma expressão muito pequena

## Slide 13: How to explore Yang data models
Notes: Cisco YANG Suite provides a set of tools and plugins to learn, test, and adopt YANG programmable interfaces such as NETCONF, RESTCONF, gNMI and more.
Its vendor agnostic and you can upload yang models directly from the router or switch, or from github.
Its downloadable in a container, easy to install go try it

## Slide 14: producer layer
Time intervals definitions for the models

## Slide 15: Publication options
On-Change
Periodic
Event notifications (failed login, optics fault, etc)
State and Configuration
Time based publications
Minimum interval 1s

## Slide 16: Telemetry taxonomy
Model-Driven Telemetry
Event-Driven Telemetry
Model-Driven Telemetry
Router X
Router X
Time
100 Interfaces UP/ 0 Down
100 Interfaces UP/ 0 Down
100 Interfaces UP/ 0 Down
99 Interfaces UP/ 1 Down
99 Interfaces UP/ 1 Down
Time
100 Interfaces UP/ 0 Down
99 Interfaces UP/ 1 Down

## Slide 17: exporter layer
Encoding and transportation for the models
gNMI
gRPC
NETCONF
RESTCONF
SNMP
CLI
It’s all about the
Apey Eyes
APIs
Get it!?

## Slide 18: MDT modes, dial-in vs dial-out
Broader flexibility in transport options
No need to open ports for inbound management traffic
Anycast & Load-balancing
Dial-out
Dial-in
A single channel (config and streaming)
Listening port on the router
No MDT configuration on the router
Only gRPC/gNMI available

## Slide 19: analytics layer
Data collection and processing

## Slide 20: Analytics stack - tig
NETWORK

## Slide 21: architecture

## Slide 22: Try it! No, really try it!!
TIG MDT Docker Container
Separate Container
https://github.com/DataKnox/Cisco-MDT-TIG-Docker
https://github.com/CiscoDevNet/yangsuite

## Slide 23: Precision!

## Slide 24
Notes: Having the ability to query a DB for all the information present in the cli shows commands, the sky is your limit for dashboarding

## Slide 33: Less intrusive and more agile monitoring
Storm Control
Optics

## Slide 34: Performance measurment

## Slide 35: Segment routing feature stack

## Slide 36: Performance Measurement
Query's sent every 1s (default 3s)
Probes completed after 10 query's
Timestamps added in hardware
PM Query format: RFC 5357 (TWAMP) or RFC 6374 (MPLS)
Extracted values: Max, Min, Average, Variance, Query's sent/received
1
2
PM Query Packet
PM Response Packet
TX Timestamp T1
TX Timestamp T4
TX Timestamp T2
TX Timestamp T3
Measurement mode:
One-Way (T2-T1)
Two-Way (T4-T1)
Loopback
Probes type:
Interface
Endpoint
SR-TE

## Slide 37: Lisbon-Porto through the coast vs interior of country

## Slide 38: Ncs vs asr plataforms

## Slide 39: Dashboard interface mode

## Slide 40: Dashboard endpoint mode

## Slide 41: Network map

## Slide 43: Backbone and core

## Slide 44: Access ring example

## Slide 46: bugs…. ups
In IOS-XR release 7.3.1 perf-meas probes weren’t working on BVI’s interfaces
In release 7.5.2 they didn’t work on ES MH-SFA, MH-AA-PA
For endpoint mode there wasn’t a yang model for last probe result
Beginning 24.1.x release fixed all the above, but broke all ipv6 endpoint probes
IOS-XE Catalyst switches had random drops – fixed in 17.12.1
Many TAC cases opened, a lot of calls and countless hours wasted….

## Slide 47: Thank you!
  FCT|FCCN
  Network Services Area Manager
  João Silva joao.silva@fccn.pt
  Over and Out!