## Slide 1
Alexander Gall
alexander.gall@switch.ch
SIG-NOC 22, Prague
2.4.2025
Unsampled Netflow Generation at SWITCH

## Slide 2
Why Unsampled?
Not necessary for volume-based metrics, but e.g.
Fine-grained analysis of security incidents
Reliable network problem debugging for low-volume flows, e.g.
  TCP handshake
  DNS transactions
Also: because we can :)

## Slide 3
Basic Architecture
These days, routers can’t produce unsampled Netflow due to resource limitations
At SWITCH, we moved to external flow generation with the deployment of the ASR9k platform
Only generate flows on external links
2015: commercial solution with the Flowmon Probe (hardware accelerate)
2020: Replace with pure software implementation on commodity hardware

## Slide 4
Per-PoP Exporter Architecture
SWITCH border router
Foreign BR1
8-port splitter
Packet Broker
Netflow exporter
Foreign BR2
Foreign BR3
Foreign BR8
adds vlan for each “color“ so we know where packets came from
Vlan 151
Vlan 152
Vlan 153
Vlan 154
Vlan 155
Foreign BRx
Vlan 156
Vlan 165
Vlan 166

## Slide 5
Packet Broker
P4-programmable, based on Tofino NPU from Intel (formerly Barefoot Networks)
Devices from Edgecore
  WEDGE 100BF-32X (32xQSFP, 6.4 Tbps)
  AS9516-32D (32xQSFP-DD, 25.6 Tbps)
In-house developed P4 program https://github.com/alexandergall/packet-broker
Other useful features (packet-mirroring)

## Slide 6
Exporter
1RU x86-based server, Intel/AMD 12-48 cores
Mellanox ConnectX5/6/7 NIC (2x100, 1x400 Gbps)
In-house developed IPFIX-compliant exporter based on the Snabb framework https://github.com/snabbco/snabb/tree/master/src/program/ipfix
Runs in user space, includes NIC driver (pre-dates XDP, DPDK)
Uses Lua with LuaJIT (very fast tracing JIT compiler)

## Slide 7
Performance
Depends on IPFIX template
Basic 5 tuple: ~500 cycles per packet (5-7 Mpps/core)
Plus ASN, MAC, VLAN, HTTP, HTTPS: ~1500 cpp (2-2.5 Mpps/core)
Uses hardware/software RSS to scale well with the number of cores
Aggregate typical rates @SWITCH: 400-600kfps, 20-25Mpps, 150-200Gbps